## Slide 1
Reinforcement-Learning-Based Job-Shop Scheduling for Intelligent Intersection Management
Shao-Ching Huang1, Kai-En Lin1, Cheng-Yen Kuo1, Li-Heng Lin1,
Muhammed O. Sayin2, Chung-Wei Lin1
1National Taiwan University, 2Bilkent University
April 2023

## Slide 2: Outline
Introduction
Background
Problem Definition
Our Approach
Experimental Results
Conclusion

## Slide 3: Intelligent Intersection Management
C. Liu et al., "Distributed conflict resolution for connected autonomous vehicles," 2018.

## Slide 4: Reinforcement Learning (RL)
An agent interacts with an environment and learns a policy from its interaction experiences
Left Figure Source: https://www.ualberta.ca/science/news/2019/november/robots-help-study-reinforcement-learning.html Right Figure Source: https://www.youtube.com/live/B4RZw9kDXKc?feature=share

## Slide 5: Motivations
Issue of state space explosion
  We need to simplify how we represent an intersection
Applicability to general intersections
  We need a general intersection model while keeping simplicity
Graph Neural Network (GNN)
  Can we utilize any kind of graphs in intersection management?

## Slide 6: Contributions
Apply RL to a graph-based intersection model
  Bridge intersection management and RL with the Job-Shop Scheduling Problem (JSSP)
  Utilize GNN and Proximal Policy Optimization (PPO) to improve performance
Identify weakness of the learning-based approach and propose potential solutions
  Grouping strategy
  Alternative heuristic policy when traffic density is low

## Slide 7: Outline
Introduction
Background
Problem Definition
Our Approach
Experimental Results
Conclusion

## Slide 8: Graph-Based Intersection Model
Conflict zone
  Crossing location of two trajectories
  One vehicle at a time
Conflict Zone
Y.-T. Lin et al., "Graph-based modeling, scheduling, and verification for intersection management of intelligent vehicles," 2019.

## Slide 9: Graph-Based Intersection Model
Timing Conflict Graph (TCG)
  Type-1 Edge: same vehicle's trajectory
  Type-2 Edge: conflicts between different vehicles from the same lane
  Type-3 Edge: conflicts between different vehicles from different lanes
D
A
B
C
4
1
2
3
1,A
1,B
1,C
2,A
3,C
3,D
4,D
4,A
Type-1
Type-2
Type-3
Y.-T. Lin et al., "Graph-based modeling, scheduling, and verification for intersection management of intelligent vehicles," 2019.

## Slide 10: Job Shop Scheduling Problem (JSSP)
Example: a JSSP instance with 3 jobs and 3 machines, and one of its possible solutions
2hr
1hr
5hr
4hr
3hr
3hr
1hr
2hr
M1
M3
M2
Machine
M1
2hr
M3
3hr
M2
1hr
Operation
M3
5hr
M2
3hr
M1
1hr
M2
4hr
M1
2hr
Job 3
Job 2
Job 1

## Slide 11: Graph-based Formulation of JSSP
A JSSP instance can also be modeled as a mixed graph
C. Zhang et al. proposed a reinforcement-learning-based approach to solve the graph-based JSSP
M1
M3
M2
M3
M2
S
M1
M2
M1
C. Zhang et al., "Learning to dispatch for job shop scheduling via deep reinforcement learning," 2020.
M1
2hr
M3
3hr
M2
1hr
M3
5hr
M2
3hr
M1
1hr
M2
4hr
M1
2hr

## Slide 12: Outline
Introduction
Background
Problem Definition
Our Approach
Experimental Results
Conclusion

## Slide 13: Problem Definition
An intersection I = (Z, T)
  Z: the set of conflict zones
  T: the set of all possible trajectories
A set of incoming vehicles X, where xi = (ri, ti) ∈ X
  ri: the expected arrival time of vehicle xi
  ti ∈ T: the trajectory of vehicle xi
Given (I, X), the corresponding TCG G = (V, E) can be consturcted
  Choose one edge (to be removed) from each pair of Type-3 edges
  Guarantee safety (no collision), automatically satisfied by conflict zones
  Guarantee liveness (no deadlock)

## Slide 14: Outline
Introduction
Background
Problem Definition
Our Approach
Experimental Results
Conclusion

## Slide 15: Our Approach
Graph-Based
Intersection Model
Reinforcement
Learning
JSSP
GNN
Batches of Incoming Vehicles
(Grouping Strategy)
Centralized Learning-Based
Intersection Manager

## Slide 16: Our Approach
Step 1. Build a timing conflict graph based on the information of incoming vehicles
  Optionally split vehicles into smaller groups for better performance
Step 2. Transform the timing conflict graph into a JSSP graph-based formulation with additional constraints
Step 3. Use the learned policy to solve the JSSP
Step 4. Use the scheduling results to improve the policy

## Slide 17: Building Timing Conflict Graph
Step 1. Build a timing conflict graph based on the information of incoming vehicles
D
A
B
C
1
2
3
1,A
1,B
1,C
2,A
3,C
3,D
3,A
Type-1
Type-2
Type-3

## Slide 18: TCG and Constrained-JSSP Transformation
Step 2. Transform the timing conflict graph into a JSSP graph-based formulation with additional constraints
  Blocking Constraint: A machine will only be released if the next operation of its previous associating job is scheduled
  Deadlock Constraint: Operations that will cause deadlocks should not be scheduled
  Arrival Time Constraint: Each operation should be assigned with a start time ≥ arrival time
1,A
1,B
1,C
2,A
3,C
3,D
3,A
S

## Slide 19: RL Formulation
Step 3. Use the learned policy to solve the JSSP
Schedule 1,A
Scheduled
Schedulable
Unschedulable
Determined
Undetermined
1,A
1,B
1,C
2,A
3,C
3,D
3,A
S
1,A
1,B
1,C
2,A
3,C
3,D
3,A
S

## Slide 20: Training
Step 4. Use the scheduling results to improve the policy
Proximal Policy
Optimization
JSSP Graph
Representation
Graph Neural
Network
Actor
Critic
Environment
Trajectories
Action
Loss

## Slide 21: Our Approach
Graph-Based
Intersection Model
Reinforcement
Learning
JSSP
GNN
Batches of Incoming Vehicles
(Grouping Strategy)
Centralized Learning-Based
Intersection Manager

## Slide 22: Outline
Introduction
Background
Problem Definition
Our Approach
Experimental Results
Conclusion

## Slide 23: Experimental Setting
Baseline: the iGreedy policy
  A greedy algorithm that schedules a vehicle to enter its next conflict zone without creating a deadlock once the conflict zone is available
Traffic density: 0.3 or 0.7 vehicle per lane per second
Group size: 10 or 30
Intersection:
Intersection IA
Intersection IB
Intersection IC
Intersection ID

## Slide 24: Exp 1. Intersection and Traffic Density
Chart: Gap to Optimal Solution
| E1 | E2 | E3 | E4
PPO(E1) | 0.624 | 0.25 | 0.437 | 0.203
PPO(E2) | 0.438 | 0.226 | 0.553 | 0.279
iGreedy | 0.292 | 0.438 | 0.12 | 0.175
Our learning-based policy usually performs better if training and validation environments are similar
 | Intersection | Traffic Density | Group Size
E1 | IA | 0.3 | 10
E2 | IA | 0.7 | 10
E3 | IB | 0.3 | 10
E4 | IB | 0.7 | 10
Environments

## Slide 25: Exp 1. Intersection and Traffic Density
 | Intersection | Traffic Density | Group Size
E1 | IA | 0.3 | 10
E2 | IA | 0.7 | 10
E3 | IB | 0.3 | 10
E4 | IB | 0.7 | 10
Our learning-based policy usually performs better if training and validation environments are similar
Chart: Gap to Optimal Solution
| E1 | E2 | E3 | E4
PPO(E3) | 1.718 | 0.608 | 0.231 | 0.168
PPO(E4) | 1.711 | 0.618 | 0.259 | 0.141
iGreedy | 0.292 | 0.438 | 0.12 | 0.175
Environments

## Slide 26: Exp 2. Group Size
 | Intersection | Traffic Density | Group Size
E2 | IA | 0.7 | 10
E5 | IA | 0.7 | 30
Chart: Gap to Optimal Solution
| E5
PPO(E2) | 1.009
PPO(E5) | 0.828
PPO(E2)+Grouping | 0.761
iGreedy | 0.839
Grouping strategy can boost performance and efficiency
Required validation time is not linear to validation group size
Environments

## Slide 27: Exp 3. Overall Comparison
Chart: Gap to Optimal Solution
| E1 | E3 | E6 | E8
PPO | 0.438 | 0.259 | 0.402 | 0.143
iGreedy | 0.292 | 0.12 | 0.261 | 0.179
 | Intersection | Traffic Density | Group Size
E1 | IA | 0.3 | 10
E3 | IB | 0.3 | 10
E6 | IC | 0.3 | 10
E8 | ID | 0.3 | 10
The iGreedy policy generally performs well when the traffic density is lower
Environments

## Slide 28: Exp 3. Overall Comparison
Chart: Gap to Optimal Solution
| E2 | E4 | E7 | E9
PPO | 0.226 | 0.141 | 0.28 | 0.206
iGreedy | 0.438 | 0.175 | 0.293 | 0.261
 | Intersection | Traffic Density | Group Size
E2 | IA | 0.7 | 10
E4 | IB | 0.7 | 10
E7 | IC | 0.7 | 10
E9 | ID | 0.7 | 10
Our learning-based policy outperforms the iGreedy policy when the traffic density is higher
Environments

## Slide 29: Outline
Introduction
Background
Problem Definition
Our Approach
Experimental Results
Conclusion

## Slide 30: Conclusion
We propose a learning-based centralized intersection manager
  Graph-based intersection modeling gives generality
  Reinforcement learning pushes the limit of scheduling performance in complex environments
  Grouping strategy improves validation performance and efficiency
Future directions
  Training acceleration
  Improve grouping strategy
  Cross-model scheduling metrics

## Slide 31
Q&A